## Slide 1
Hardware Accelerator for DNA Local Sequence Alignment
Author: Eliyahu Wiener
Supervisor: Zuher Jashan
VLSI LAB
Winter 2025

## Slide 2: General Information
What is Sequence Alignment?
Comparing (ordering) DNA, RNA, or protein sequences
Identifies regions of similarity
Used in bioinformatics for evolutionary studies and gene function prediction

## Slide 3: Global vs Local Alignment
Global Alignment:
Compares entire sequences
Best for sequences of similar length
Example: Needleman-Wunsch Algorithm
Local Alignment:
Finds regions of high similarity within sequences
Best for analyzing genetic variations and functional domains
Example: Smith Waterman Algorithm

## Slide 4: Smith Waterman Algorithm
Dynamic programming algorithm.
Analyzes and compares sequence segments of varying lengths to maximize similarity scores.
Time complexity:
Space Complexity:

## Slide 5: Smith Waterman Algorithm Steps
Step 1: Initialization
  Create a scoring matrix with rows and columns for both sequences.
  First row and first column are initialized to zero.
Step 2: Matrix Scoring
  Assign scores for matches, mismatches, and gaps.
  The formula:
    Match: +1
    Mismatch: -1
    Gap Penalty: -2
Step 3: Traceback
  Start from highest scoring cell in the matrix.
  Trace back until reaching a zero score.
  Reconstruct the best alignment.

## Slide 6: Smith Waterman Algorithm

## Slide 7: Smith Waterman Algorithm - Example
Step 1: Initialization

## Slide 8: Smith Waterman Algorithm - Example
Step 2: Matrix Scoring

## Slide 9: Smith Waterman Algorithm - Example
Step 2: Matrix Scoring

## Slide 10: Smith Waterman Algorithm
Step 3: Traceback

## Slide 11: Smith Waterman Algorithm
Step 3: Traceback
Alignment 1 Alignment 2 Alignment 3
GCA GCATAG GCATAGGT
GCA GCA-AG GCA-AGCT

## Slide 12: Motivation – Why Hardware Acceleration?
Challenges in Sequence Alignment
1. Large genomic datasets
require significant computational power.
2. Software solutions
(e.g., running Smith-Waterman on CPUs) are too slow.
3. Millions of alignments
may be needed in bioinformatics databases.

## Slide 13: Motivation – Why Hardware Acceleration?
Why Hardware?
1. Faster processing
by leveraging parallelism.
2. Reduces bottlenecks
in computing large sequences.
3. Improves efficiency
by offloading computation to specialized hardware

## Slide 14: Solutions
Manual Alignment: Simple but impractical for large sequences
Software-Based Dynamic Programming: Accurate but computationally expensive
Heuristic & Probabilistic Algorithms: Fast but less accurate
Hardware Accelerators: Best balance of speed, efficiency, and accuracy

## Slide 15: Chosen Solutions Principles
Smith-Waterman Algorithm implemented in hardware
Parallel processing to improve speed
Dedicated hardware accelerator reduces computational overhead
Time Complexity: O(n)
Space Complexity: O(n²)

## Slide 16: Top Design

## Slide 17: General Architecture

## Slide 18: General Architecture
Processing Strategy:
  Tile-based computation
  Parallel processing for efficiency

## Slide 19: Data Representation
Input Encoding:
A = 00, T = 01, C = 10, G = 11
Output Encoding (Including Gaps):
A = 000, T = 001, C = 010, G = 011, Gap = 100

## Slide 20: Processing Flow
Input Sequences (256 characters each)
Scheduler Divides Matrix into Tiles (16×16)
Parallel Computation:16 Solver Units process tiles concurrently
Organizer Collects Results
CIGAR Builder Constructs Final Alignment

## Slide 21: Block Level Diagram - Scheduler
Distributes sequence data to solvers

## Slide 22: Block Level Diagram - Solver
Compute Smith-Waterman scoring

## Slide 23: Block Level Diagram - Organizer
Manages results, tracks global max score

## Slide 24: Block Level Diagram - RAM
Stores intermediate data

## Slide 25: Block Level Diagram - CIGAR Builder
Performs traceback and constructs the alignment

## Slide 26: HDL Implementation – Solver
Components:
State Machine (IDLE, INIT, PROCESS_DIAG, FINALIZE)
Data Structures:
  Score Matrix
  Arrow Matrix
Processing Algorithm:
  Match/Mismatch Scoring
  Gap Penalty Application
  Traceback Computation

## Slide 27: HDL Implementation – Organizer
Functionality:
Collects solver results
Tracks max score
Stores data in RAM
Manages traceback coordination

## Slide 28: Simulating the Solver
Testbench Setup:
Clock and reset signals initialization.
Input test cases for sequences and scores.
Validation of:
Correct alignment generation.
Proper score calculation.
Timing constraints compliance.

## Slide 29: Simulating the Organizer
Test Scenarios:
RAM read/write tests.
Solver interactions:
Handling multiple solver completions.
CIGAR Builder interface:
Verifies correct traceback reconstruction.

## Slide 31: Uncomplete tasks and Further Work
Saving trace per tile
Streaming the input
Addressing the memory
Simulations results visualization
Synthesis of the HDL Implementation
Layout
Comparing performance – hardware vs software

## Slide 32: Conclusions
Hardware accelerators provide a faster, more efficient way to align DNA sequences.
Designing for parallelism and concurrency is crucial.
The Smith-Waterman algorithm benefits from dedicated hardware execution.
This project demonstrates how hardware acceleration can enhance bioinformatics applications.